## Slide 1: Heartbleed
Originally prepared by: Haichao Zhang (Samsung Research)
Modified by: Chetan Jaiswal (Truman State)

## Slide 2: Plan
1. Environment set up and preparation.
2. Introduction & background about the attack.
3. Perform the attack.
4. Questions & discussions.

## Slide 3: Environment set up
2 VMs required:
One as the https server, one as the attacker.
Both uses NAT-Network adaptor.

## Slide 4
SSL/TLS: a secure protocol
The packet will be encrypted and signed to defeat the sniff & spoof attack.
e.g. https uses such technique to ensure the banking, and other confidential activity on the Internet.
Secure!
Secure?

## Slide 5
Heartbeat protocol
It is part of the TLS/SSL to keep the connection alive even though there may be some gap between each communication.
Since it is quite expensive to build the SSL/TLS channel (key exchange, PKI, etc. require a lot of time), this is a cheaper compromise.

## Slide 6
I want to know whether my connection is still alive…
Server, are u still there? if so, return “ABC”(3 characters) to me.
TLS/SSL
User wants the message “ABC”(3 characters)
“ABC” (3 characters)
Both of us are still connected. We should keep the connection alive…
TLS/SSL
TLS/SSL
TLS/SSL
TLS/SSL

## Slide 7: OpenSSL: Implementation of SSL/TLS
OpenSSL is a widely used open-source SSL/TLS library; However, when implementing SSL/TLS protocol, OpenSSL didn’t do it in a right way…

## Slide 8
Type(request)
Payload[Payload_length]
Padding[padding_length]
Payload_length
Type(response)
Payload[Payload_length]
Padding[padding_length]
Payload_length
“ABC”
Memory
=
Request packet
Response packet
Heartbeat: OpenSSL Implementation

## Slide 9
Type(request)
Payload[Payload_length]
Padding[padding_length]
Payload_length
Heartbeat: packet structure in Python style

## Slide 10
Replaced by 0x03,0xEF # payload length = 1022
Type(request)
Payload[Payload_length]
Padding[padding_length]
Payload_length+1000
Possibility: Payload_length inconsistency

## Slide 11
Type(request)
Payload[Payload_length]
Padding[padding_length]
Payload_length+1000
Type(response)
Payload[Payload_length+1000]
Padding[padding_length]
Payload_length+1000
Memory
=
Extra data
“ABC”
Request packet
Response packet
Possible Attack: on the server side

## Slide 12: Mission Accepted
Explore the Heartbeat process to find out the possible attack on SSL/TLS

## Slide 13: Server VM: https web server
We have built-in a https webserver www.heartbleedlabelgg.com on each VM.
The website uses elgg engine

## Slide 14: Attacker VM: Set up the DNS
Modify the attacker machine’s DNS setting. (/etc/hosts file)
VM1: https server
VM2: attacker machine
Testing whether you did it right (on the attacker VM):
$ ping www.heartbleedlabelgg.com
You should find the response is from the IP of the https server VM.

## Slide 15: Download the attack.py to the attacker VM
This is the program we modified for our lab.
  attack.py
Don’t forget to use the command to make executable:
$ chmod 755 attack.py
or
$ chmod a+x attack.py

## Slide 16
Type(request)
Payload
Padding
Payload_length
attack.py: general flow
Type(request)
Payload[22]
Padding
Payload_length
Construct
Heartbeat
request
Controlled by user input

## Slide 17: Utility of the program
Message printed:
The program specially compares the payload length between the request and the response to tell the user whether the server is vulnerable or not.
The program will dump the payload buffer to the screen: the bytes that cannot be printed in ASCII code will be ignored (e.g. 0x00)

## Slide 18: Set the payload_length value
In the program, we provide an option to set the value accordingly:
./attack.py www.heartbleedlabelgg.com –l 0x4000
./attack.py www.heartbleedlabelgg.com –l 33
./attack.py www.heartbleedlabelgg.com # the length set to 0x4000 by default

## Slide 19: Task 1: play with the program attack.py
Run the program with different payload_length:
Is the server vulnerable?
What is the boundary between a benign payload_length and a malicious (Heartbleed) one?
Do you get anything useful for an attacker?

## Slide 20: Real Attack: find the admin password
Nothing useful we get from our attack.py
This is because the server’s memory is empty and no meaningful data is stored.
So, we move to the server VM and do something to allow some meaningful data inside the memory. For example, open the website www.heartbleedlabelgg.com with firefox and perform a login.
Username: admin
Password: seedelgg
HTTPS server requires the certificate signed by a qualified CA or it will throw a warning on the browser. We didn’t pay any CA for a real certificate, so you will have to add an exception for www.heartbleedlabelgg.com

## Slide 21: Real Attack 2: steal a secret message
Use admin to write a private message to any member in the site. Repeat the previous process and try to find out the secret.

## Slide 22: Ubuntu: Quick way to fix the vulnerability
$ sudo apt-get update
$ sudo apt-get upgrade

## Slide 23
unsigned char *p = &s->s3->rrec.data[0], *pl;
unsigned short hbtype;
unsigned int payload;
unsigned int padding = 16; /* Use minimum padding */
/* Read type and payload length first */
hbtype = *p++;
//! extracting the length of the payload from the heartbeat request package
n2s(p, payload);
pl = p;
if (s->msg_callback)
s->msg_callback(0, s->version, TLS1_RT_HEARTBEAT,
&s->s3->rrec.data[0], s->s3->rrec.length,
s, s->msg_callback_arg);
if (hbtype == TLS1_HB_REQUEST)
{
unsigned char *buffer, *bp;
int r;
/* Allocate memory for the response, size is 1 byte
* message type, plus 2 bytes payload length, plus
* payload, plus padding
*/
buffer = OPENSSL_malloc(1 + 2 + payload + padding);
bp = buffer;
/* Enter response type, length and copy payload */
*bp++ = TLS1_HB_RESPONSE;
s2n(payload, bp);
memcpy(bp, pl, payload); //
/* Random padding */
RAND_pseudo_bytes(p, padding);
Copy the string without checking the integrity for $payload
Read the length variable and store in $payload
from the packet

## Slide 24
0x01(request)
22 bytes Payload
padding
0x80,0x00(length=32K)
Memory
0x02(response)
32K bytes Payload
padding
0x80,0x00(length=32K)
response packet
Request packet
22 bytes Payload
Login=Alice;Password=alice123;… Elgg/action/sendMsg:&sender=Kate&title=HappyBirthday.&SSL_Private_key=2G$FDAF23430!\&^BDFF32TT*54$3345(11*KFF89XZ16
… ...
… …
… …
32K – 22 byte
32 KB
int payload
memcpy(bp, pl, payload)
n2s(p,payload);
s2n(payload, bp);
summery

## Slide 25
unsigned char *p = &s->s3->rrec.data[0], *pl;
unsigned short hbtype;
unsigned int payload;
unsigned int padding = 16; /* Use minimum padding */
/* Read type and payload length first */
hbtype = *p++;
//! extracting the length of the payload from the heartbeat request package
n2s(p, payload);
pl = p;
if (s->msg_callback)
s->msg_callback(0, s->version, TLS1_RT_HEARTBEAT,
&s->s3->rrec.data[0], s->s3->rrec.length,
s, s->msg_callback_arg);
if (hbtype == TLS1_HB_REQUEST)
{
unsigned char *buffer, *bp;
int r;
/* Allocate memory for the response, size is 1 byte
* message type, plus 2 bytes payload length, plus
* payload, plus padding
*/
buffer = OPENSSL_malloc(1 + 2 + payload + padding);
bp = buffer;
/* Enter response type, length and copy payload */
*bp++ = TLS1_HB_RESPONSE;
s2n(payload, bp);
memcpy(bp, pl, payload); //
/* Random padding */
RAND_pseudo_bytes(p, padding);
+ hbtype = *p++;
+ n2s(p, payload);
+ if (1 + 2 + payload + 16 > s->s3->rrec.length)
+ return 0; /* silently discard per RFC 6520 sec. 4 */
+ pl = p;
+
Add
checking

## Slide 26: Extra thinking
If the payload_length is the problem, why don’t just remove this field?